## Slide 1: REGULATED MATERIALS/WASTE HANDLING FOR GREATER MN
Environmental Investigation Unit
Office of Environmental Stewardship
2019

## Slide 2: GENERAL
Place wastes in sturdy containers with no dents or rust.
Keep areas around containers clear and uncluttered.
Keep waste container lids and bungs closed at all times except when adding wastes.

## Slide 3: LABEL ALL CONTAINERS
All containers need to be labeled of its contents.

## Slide 4: When Ordering Products
Use MnDOT Inventory!
  Use Approved Products List
  Ask these questions:
    Is this the least hazardous option?
    Is the product ordered just enough to do the job?

## Slide 5: WHEN MANAGING A WASTE
Use Safety and Inventory personnel
  As an information source
  Waste consolidation
  Disposal
  Approved end sites
  Record keeping

## Slide 6: EMPTY DRUMS
Store on side.
At a designated location.

## Slide 7: No Trash Burning

## Slide 8: Store Containers Holding Products or Waste Out of the Outside Elements

## Slide 9: Housekeeping
Flammable Storage Cabinets
Keep common area for used Oil Storage and Change out clean/swept
Fence Lines

## Slide 10: USED OIL
Used oil can be burned on site for heat.
Can be transported by MnDOT personnel
  if >55 gallon container, contact Safety.

## Slide 11: USED OIL
Includes: motor oil, transmission fluid, lubricating oil, hydraulic oil, power steering fluid, brake fluid, and gear oil.
Does not include: solvents/thinners, gasoline, degreasers, or any other waste.

## Slide 12: USED OIL BURNERS
Must have On-Spec used oil analysis.

## Slide 13: USED OIL FILTERS
Drain a minimum of 24 hours.
Place into “used oil filter” drum AND Cover.

## Slide 14: USED OIL SORBENTS
Re-use sorbents material as much as possible.
Recycle sorbents; do not throw in trash.
Sorbents soaked with liquids other than used oil (solvents, etc.) should be kept in a separate container.

## Slide 15: DO NOT MIX!
Used Oil Sorbents
  Oil rags have the option of laundry service
Oil Filters
Store In Separate containers…

## Slide 16: CLEANING USED OIL LUBE CUBES
Use Approved Contractors to clean.
OSI, Minnesota Petroleum/MnBlue, Etc.

## Slide 17: USED ANTIFREEZE
Do not put into storm sewer or septic tank.
Use a MnDOT approved contractor
Can discharge to a WWTP (Wastewater Treatment Plant) with permission from the WWTP.
  Must keep records showing amount of waste antifreeze generated.

## Slide 18: USED LEAD-ACID BATTERIES
Send to HQ for proper management
Must be stored on acid resistant surface/curbing, with no floor drains.
  plastic tub
  Asphalt
  Rubber
  concrete with an acid
  resistant coating.

## Slide 19: What’s Wrong???

## Slide 20: USED DRY CELL BATTERIES
Alkaline and 6V lithium batteries can be thrown in the trash.
Other batteries must be collected in a designated storage location
Tape ends with electrical/duct tape or store in baggies separately.

## Slide 21: Battery Fire

## Slide 22: PARTS WASHER WASTE
MnDOT has found it cost effective to filter and reuse.
If liquid is determined to be a waste
Place in empty, clean drum.
Contact District Safety Administrator for proper management.
Keep lids and bungs closed, except when adding.

## Slide 23: WASTE PARTS WASHER FILTERS
Dispose with burnable used oil sorbents if fiber.
Dispose with used oil filters if metal.

## Slide 24: AQUEOUS PARTS WASHER OIL SKIMMERS
Mix with used oil.

## Slide 25: OLD PAINTS, SOLVENTS, AEROSOL PRODUCTS
If over 10 years old, time to get rid of…
Beyond shelf life

## Slide 26: PAINT WASTE
MnDOT has found it most cost effective to use disposable paint brushes.
Recycling paint is free; contact your District Safety person for recycling paint.

## Slide 27: WASTE PAINT SOLVENT
Use products through inventory
MPCA’s “F” list
Lacquer Thinner
  Watch out…
Don’t Use!
If you must use, must handle all rags as HW!!

## Slide 28: Solvents
Preferred: Mineral Spirits
Acceptable: Xylene and Acetone

## Slide 29: WASTE AEROSOL CANS
Empties can go in the trash.
Manage partially full unusable cans as hazardous waste.
Remove Stems/Nozzles
No picks or hammer claws.

## Slide 30: Waste Aerosols
Don’t mix with other wastes! (below picture found in drum)
Also, watch for F-listed wastes in aerosols!

## Slide 31: Asphalt Sludge
Cannot Dispose on asphalt piles.
Must containerize
  Non hazardous
  Label as Asphalt Sludge
  Small amounts may be added to
  used oil sorbents

## Slide 32: USED FLUORESCENT BULBS
Do not crush or break.
Do not tape together.
Store in original boxes or other boxes of similar size.
If lamps break, store in sealed, labeled container.
Label containers “Waste Lamps” or “Used Lamps“ and Date.
Store in a designated location.

## Slide 33: Fluorescent Bulb No-No’s

## Slide 34: WASTE BALLASTS/CAPACITORS
Treat as hazardous unless it states “No PCB’s”.
Label must be visible.

## Slide 35: SPILL CONTROL
Absorbent
Spec Approved Container
Non-Spark Producing (aluminum) Shovel

## Slide 36: FLAMMABLE / SEDIMENT WASTE TRAPS
Top - Oil layer - Dispose with Oil Sorbents
Middle - Water layer - Down the Drain
Bottom - Sand layer – MPCA permitted Sanitary/Industrial Landfill

## Slide 37: Good Housekeeping of Sediment Traps
Clean spills immediately
  Prior to going down drain
Keep containers closed
Keep floors clean
  Sweep
  Drip pans
No dumping liquid wastes
  Solvents, oils, etc.
Clean sediment traps periodically

## Slide 38: Flammable Trap/Waste Oil
Sorbent pads are hydrophobic
Sits on the top oily layer
Dispose with oil sorbents

## Slide 39: WASTE TRAP SAND Industrial Waste
Stored away from outside elements.
  In building
  Covered
Dispose of in a MPCA permitted sanitary landfill or MPCA permitted industrial landfill.
  Not a demolition landfill.
Another option is manage at an asphalt plant.

## Slide 40: Waste Trap Sand
No Land Application
  Salt is the main concern; will not evaporate or biodegrade. It will remain and migrate to groundwater and surface water.
No Sand Piles
  Placement on a sand pile is considered land application.

## Slide 41: Septage Waste
No land application, unless approved by Neile Reider.

## Slide 42: STREET SWEEPINGS/GRIT CHAMBERS
¾” Screen
Does not pass through, dispose at a MPCA permitted sanitary landfill.
Does pass through,
  Sub-base, Fill, Concrete
  IF, 100 ft from water/drainage, 3 ft above groundwater, 10 ft above fractured bedrock

## Slide 43: STREET SWEEPINGS/GRIT CHAMBERS
OR
Dispose of at an MPCA permitted sanitary landfill or MPCA permitted industrial landfill

## Slide 44: Problems with Hiring Contractor to Clean (waste traps, holding tanks, septage)
Internal Audit Findings:
Unknown to where sediment sand is going
Contractor is land farming sediment sand and septage

## Slide 45: Removal Contracts (waste traps, holding tanks, septage)
Specify
  End sites
  End site documentation
    Proof of disposal
Follow the MnDOT guidance document!

## Slide 46: TREATED WOOD WASTE
Disposal at MPCA permitted sanitary or industrial landfill
  Keep documentation on file (eDOCS).

## Slide 47: TREATED WOOD WASTE
Can
Reuse in original form or use in secondary applications such as fence posts, landscaping, or other projects.
Cannot
Chip and reuse (landscaping).
Burn in brush pile.
Bury.

## Slide 48: Cabinet Style Abrasive Blasters
Must sample and laboratory analysis prior to disposal. (Harold B.)

## Slide 49: Waste Tires
Store in a designated storage area.
Inventory center will make arrangements with the vendor on contract for the pick up.

## Slide 50: WASTE ELECTRONICS
Computer parts, TVs, etc.
Store out of the elements
Notify Inventory
  Palletized
  MnDOT approved recycling facility.
  State Surplus Program
Road Finds…
  DO NOT THROW IN TRASH!

## Slide 51: Herbicide Storage
Secondary containment

## Slide 52: Waste Lead Solder
Containerize
Label container
  Hazardous Waste
  Waste solder

## Slide 53: STAINS ON SAND PILE OR GROUND
Should not be disposed of in or on sand piles or ground…
  Sloppy practices…

## Slide 54: Salt Storage - Poor

## Slide 55: Salt Storage - Good

## Slide 56: SALT NOT COVERED
Includes Winter Sand

## Slide 57: Salt Release

## Slide 58: Culverts
Black Coating
AB Culverts
  Asbestos Bonded Culverts

## Slide 59: Recycling Office Materials
All truck stations need to recycle office material.
  Paper
  Containers
  Plastics

## Slide 60: SHIPPING PAPERS REQUIRED
When shipping regulated waste from the TS to the HQ, documentation is required
  VSQG consolidation program
  Available on website
    Ship To
    Ship From
    Waste
    Quantity
    Date
    One copy to truck station. One copy to HQ’s

## Slide 61: Very Small Quantity Generator (VSQG) Consolidation Program
MPCA state program
Must Follow Simple Guidelines
Transport Regulated Waste to HQ
Shipping Paper
Simple & Cost Effective
Privilege

## Slide 62: VSQG CONSOLIDATION PROGRAM BENEFITS
Get out of using:
Licensed Hazardous Waste Transporter
Hazardous Waste Manifest
Stop Charge
Storage

## Slide 63: Road Kill
MnDOT Urban Challenge

## Slide 64: Is it a tasty meal?

## Slide 65: Or Work Around It?

## Slide 66: Or maybe it takes care of itself…..

## Slide 67: Other Options
Leave on Right-of-Way ditch
Compost
Landfill
Game farm food

## Slide 68: Leave on Right-of-Way Ditch
Pull further off roadway
  No more than ¼ mile
Place on the ditch back slope.
When feasible, cover the carcass with wood chips.

## Slide 69: Compost
Follow Dept. of Agriculture publication, “Composting Animal Mortalities”

## Slide 70: Game Farm Food

## Slide 71: Questions?